## Slide 1: Infrastructure for the DBA: An Introduction
Peter Shore
SQL Saturday Chicago 2016

## Slide 2: Agenda
Introduction
Network Terms
Network Devices
Network Services
Server Hardware
Server Storage
Attached Server Storage
Virtualization
Cloud
Active Directory
Windows Server

## Slide 3: Who am I?
Platform Database Consultant – BlueChip Consulting Group
Intentionally Accidental DBA
Over 20 years IT experience
  Server Engineer
  Desktop Engineer
  Network Infrastructure
  Desk side support
President CBusPASS
Member Multiple Virtual Chapters
How to find me
  Twitter: @pshore73
  E-mail: pshore73@outlook.com
  Blog: http://shoresql.wordpress.com

## Slide 4: Network Terms
LAN
  Local Area Network
    Computer network connecting computers in a limited area
      House
      School
      Office
WAN
  Wide Area Network
    Communication network extended over a wide area
      Multiple data centers
      Internet
VLAN
  Virtual Local Area Network
    Not limited to hypervisor environments
    “Any broadcast domain that is partitioned & isolated in a computer network at the data link layer (OSI Layer2)”
    Partition traffic
    Partition security
    Does not expand bandwidth
Bandwidth vs. Latency
  Bandwidth – maximum throughput
  Latency – delay from input to outcome

## Slide 5: Network Devices
Hub
  Single broadcast domain
  Single Segment
  Mostly retired
  No commercial production beyond 100Mbps
Switch
  “Switches create networks” - Cisco
  Each port is a broadcast domain
  Managed vs. Unmanaged
  Multi-segment
  Available to 10 Gbps
Router
  Determines next network point a packet should be forwarded
  “Routers connect networks” - Cisco

## Slide 6: Network Services
Dynamic Host Configuration Protocol (DHCP)
  Delivers TCP/IP configuration
    Automatic assignment of address to end-points
    TCP/IP Address
    Subnet Mask
    Default Gateway
  Allocated by time, known as a lease
Domain Name Services (DNS)
  “Phonebook” of Names to TCP/IP addresses
  Address Records (A Records)
    Record linking address to name
  Canonical Name (C Name)
    Reference or redirection
  Mail Exchanger (MX Record)
    Identifies a mail server

## Slide 7: Wires vs. Radios
Wired
Pros
  Tier by tier higher speed
  More secure
  Better for data centers
Cons
  Lacks flexibility
  Installation cost
Wireless
Pros
  Flexible
  Enables BYOD
  Relatively lower installation cost
Cons
  Tier by tier speeds lower
  Security weaknesses

## Slide 8: Server Hardware
Server/Host/Blade
Central Processing Unit (CPU)
  Cores
  Hyper-threading
Memory (RAM)
  Random Access Memory
Non-Uniform Memory Access (NUMA)

## Slide 9: Server Storage
Local Storage
  Controller in server
  Disk in server
  Configured at server level
  Typically in Redundant Array of Inexpensive Disks (RAID)
    RAID 0 – striping no parity
    RAID 1 – mirror
    RAID 5 – striping with parity
    RAID 10 – mirror of stripes
  Peripheral Component Interconnect Express (PCIe)
    Slot on motherboard
    PCIe flash disk (example FusionIO)

## Slide 10: Attached Server Storage
External to physical server
  Behavioral nuances differ by vendor
Often used in conjunction with blade style server
Often used in virtual environments
Network Attached Storage (NAS)
  Connection to NAS Server (aka NAS head)
  Server connects to disk array
Storage Attached Network (SAN)
  Connection to storage via Host Bus Adapter
  Fibre channel dedicated hardware
  iSCSI over LAN
  Behaves more like on-board attached storage

## Slide 11: Virtualization
All most all SQL Server work loads can be virtualized
Biggest factor is hardware
Must be properly configured
Creates abstraction layer between Windows Server and hardware
Virtualization layer controls access to physical hardware
Host level memory pressure may require minimum memory setting
Viable part of High Availability solution, but not the whole solution
Backup approach can be an issue

## Slide 12: Cloud
Someone else’s datacenter
Infrastructure as a Service (IaaS)
  Virtualized servers
  Can replace most or all infrastructure
Platform as a Service (PaaS)
  Geared toward software development
  Backend systems
  Does not replace on-site infrastructure
Software as a Service (SaaS)
  Productivity software

## Slide 13: Cloud

## Slide 14: Active Directory
Microsoft implementation of Lightweight Directory Access Protocol (LDAP)
Hierarchical database
Objects organized by Organization Units
  SQL Servers separated out
  Service accounts separated out & grouped
Group Policy
  “Group Policy is an infrastructure that allows you to implement specific configurations for users and computers. Group Policy settings are contained in Group Policy objects (GPOs), which are linked to the following Active Directory directory service containers: sites, domains, or organizational units (OUs).” (http://tinyurl.com/k368u74)

## Slide 15: Active Directory
Managed Service Accounts
  Complex passwords known only to account and Active Directory
  Maintain Kerberos Service Principal Names (registering SPN http://tinyurl.com/zepmxpd)
  Computer specific
  Server 2008r2 with Active Directory Functional Level 2008r2 or higher
Group Managed Service Accounts
  Used on multiple hosts
  Not supported until SQL 2016

## Slide 16: Windows Server
TCP Chimney Offload
  Transfers workload from CPU to NIC during data transmission
  Disable it can caused connectivity problems, designed for short lived connections
Group Polices in affect
  GPResult /r
Create GPO
  Lock pages in memory
  Perform Volume Maintenance

## Slide 17: Anti-Virus
Valid arguments to both sides
If implemented use Microsoft recommendations for exceptions
http://social.technet.microsoft.com/wiki/contents/articles/953.microsoft-anti-virus-exclusion-list.aspx

## Slide 18: Questions?